## Slide 1
Transfering & Receiving of Image using Gnu Radio

## Slide 2
Modulation:
First we created a simulation for the QPSK modulation of the signal having value ranging from 0 to 255 using constellation modulator block.

## Slide 3
Channel Simulation
The next step of our simulation was to deal with the typical issues which can be faced while transferring the image for that we used the channel model block of Gnu Radio which allowed us to play with the parameters noise timing and frequency drift.This allowed us to visualize the effects of channel how it become distorted before it is received at receiver.

## Slide 4
Effects of Channel
1.Thermal Noise:
2.Timing Offset:
3.Frequency Offset:

## Slide 5
Time Recovery
Polyphase clock sync is used for this purpose this block perform multiple task
1.Perform clock recovery
2. Provide the matched filter needed to remove the Inter Symbol Interface (ISI)
3.Internally down convert the signal to desired symbol per second

## Slide 6
CMA Equalizer
1.Used for correcting multipath distortion caused to to many paths between transmitter and receiver.
Only capable of converging signal to unit circle but at any given phase it doesn’t solve the problem of phase and frequency correction.

## Slide 7
Costas Loop
To deal with the problem of frequency and the phase offset costas loop is used

## Slide 8
Decoding Process
Symbols from constellation plot is converted to bits using the demodulator and than mapped to their binary equivalents.
Differential encoding is used before modulation therefore differential decoding is used now.
Repack processing block is used to extracts bits from a stream of bytes and than reconstructs bytes with 8 bits.

## Slide 9
Issues with Model
The reconstructed byte streams were not identical to the input byte during simulation .
Later we find out that it occurred because the byte streams were misaligned. This issue was due to latency between the demodulator and modulator blocks. In effect, the demodulator does not know when to start.
Resolve this issue with Packet Encoder & Decoder

## Slide 10
Packet Encoder & Decoder
Some attributes of Packet Encoder
1.Preamble:-Used to synchronize transmission timing tells receiver that data is about to transmitted when left blank than it takes default value.
2.Payload Length:-Represent number of bytes included in each packets,larger value work better for large image

## Slide 11
Result & Conclusion
Some problem occurred while transferring image using antenna as during the initial transmission a noise burst occur which effect in corrupting the initial bytes to be transferred.
This causes the serious issue in image transferring as the first bytes in files represent the file header and due to this the received data can’t be identified as image and the file can’t be opened.Even the whole file was being transferred and the rest of the file was correct but due to corrupted header it causes image viewer to reject it.
This issue was tackled by preamble of packet encoder by increasing its length it allows the receiver to delay its starting point but it causes the speed of transmission to slow down a lot.